## Slide 1
CONCLUSION
Xiaoran Jiang, Jinglei Shi and Christine Guillemot
INRIA Rennes Bretagne-Atlantique, Rennes, France
A Learning Based Depth Estimation Framework for 4D Densely and Sparsely Sampled Light Fields
DEPTH ESTIMATION EXPLOITING LIGHT FIELDS
A SUPERVISED LEARNING BASED DISPARITY ESTIMATION SCHEME
EXPERIMENTS AND ANALYSIS
Three categories of methods:
Based on SAI (Sub-Aperture Images): Patch-based block matching
Based on EPI (Epipolar Plane Images): Slope is proportional to the disparity value
Based on refocused images
Our algorithm can be also naturally integrated into a light field view synthesis pipeline, since it is able to infer disparity information for a view that the color information is unknown.
GRAPH SIGNAL PROCESSING : GRAPH TRANSFORMS
The effectiveness of data-driven algorithms significantly depends on the quality and the quantity of training data.
Existing synthetic datasets
MIT Light Field Archive (without ground truth disparity/depth values)
HCI Light Field Dataset (dense light fields only)
Our proposed datasets
Sparse Light Field Dataset (SLFD): 53 scenes with disparity range [−20,20]
Dense Light Field Dataset (DLFD): 43 scenes with disparity range [−4,4]
Method
Deep learning based cascaded framework.
A pre-trained FlowNet 2.0 is fine-tuned by pairs of stereo images, and the obtained model is used to estimate disparity between pairs of anchor views, arranged horizontally or vertically.
These coarse estimates are then fused at each anchor viewpoint by exploiting the warping error from other anchor viewpoints.
Multi-scale residual learning for the refinement of the fused disparity map.
The propagation of disparity from anchor viewpoints towards other viewpoints is performed by an occlusion-aware soft 3D reconstruction method [5].
Purpose of the scheme
Handle either a dense or a sparse light field for disparity/depth estimation based on 4 corner views.
Generate one disparity map for each light field view.
EXPERIMENTAL RESULTS
DATASETS
[1] H.G. Jeon, J. Park, G. Choe, J. Park, Y. Bok, Y.W. Tai, and I.S. Kweon, "Accurate depth map estimation from a lenslet light field camera," in Int. Conf. on Computer Vision and Pattern Recognition, 2015.
[2] S. Zhang, H. Sheng, C. Li, J. Zhang, and Z. Xiong, "Robust depth estimation for light field via spinning parallelogram operator," J. Computer Vision and Image Understanding, 2016.
[3] X. Jiang, M. Le Pendu, and C. Guillemot, "Depth estimation with occlusion handling from a sparse set of light field views," in IEEE Int. Conf. on Image Processing, 2018.
[4] C.T. Huang, "Empirical bayesian light-field stereo matching by robust pseudo random field modeling," IEEE Trans. on Pattern Analysis and Machine Intelligence, 2018.
[5] E. Penner and L. Zhang, “Soft 3d reconstruction for view synthesis,” ACM Trans. on Graphics (Proc. SIGGRAPH Asia), 2017.
ERC advanced grant CLIM
Table 1. Quality evaluation of the estimated disparity maps on center view for dense light fields
Table 2. Quality evaluation on center view for sparse light fields
Implementation details
Data augmentation - Geometrical transformations (e.g. rotation, translation or scaling) that involve data interpolation bring extra errors in the ground truth disparity values. - Only chromatic transformation has been applied by changing the hue, saturation, contrast and brightness of training images.
Learning details - Initial learning rate set to 0.0001 for the first 500 epochs, then decreased by half every 200 epochs. - 2 days of training with a 15G GPU NVIDIA P-100.
Fusion based on warping error maps
Fine-tuned FlowNet 2.0 for disparity estimation
Drawbacks and Challenges
Most of these methods are designed for dense view sampling.
Very few methods have been proposed for sparse light fields, including deep learning approaches.
EPI-based methods only suitable for dense light field.
Needs of prior knowledge on the disparity range.
for occlusion-free areas
for non-overlapped occlusion zones
FN2: the pre-trained FlowNet 2.0 model
FN2-ft: finetuned with no constraint on view positions
DispNet-ft and FN2-ft-stereo: finetuned with stereo light field views only
Light fields:
4D: Intersection with 2 planes LF( u, v, s, t)
3D scene geometry estimation and reconstruction
approximated binary occlusion mask